#### 1. IDENTIFICATION

PRODUCT NAME: 		Husky Coil Guard

Recommended Use:		For deep cleaning air conditioning coils and associated equipment.

Manufactured for: 		Bronz-Glow Technologies, Inc.

175 Bronz Glow Way

St. Augustine, FL  32095

United States

Emergency Phone No.:              CHEMTREC: 1-800-424-9300 (US);     703-527-3887 (International)

2. HAZARDS IDENTIFICATION

HAZARD DESIGNATION

"Xi" - Irritant

R36/37/38: Irritating to eyes, respiratory system and skin.

GHS CLASSIFICATIONS

Health: Eye Irritation, Category 2

GHS LABEL

Exclamation mark

Hazard statement(s)

Signal Word: WARNING

Route of entry:     Inhalation: yes     Skin: yes     Eyes: yes     Ingestion: yes

Health Hazards (acute and chronic): This material is corrosive to skin, eyes, and internal organs.

Signs and Symptoms of Exposure:

Eye Contact: Severe irritation and possible burns.

Skin Contact: Severe irritation and possible chemical burns. Symptoms may be delayed.

Inhalation: Mists may irritate respiratory system and cause difficulty breathing.

Ingestion: Solutions and mists are corrosive and toxic. May cause gastric distress, diarrhea, and vomiting. May be fatal if swallowed.

# Medical conditions generally aggravated by exposure: Contact may aggravate pre-existing medical conditions such as dermatitis or asthma.

3. HAZARDOUS INGREDIENTS INFORMATION

INGREDIENT                 CAS NO       EINECS NO.	%	       Symbol   Risk Phrases

Water	              	 7732-18-5			60-80

Silicic acid, potassium salt 1312-76-1	                          <1.0                 C  Xi           R34,R37

Additional information: For the wording of the listed risk phrases refer to section 16.

4. FIRST AID

Inhalation: Remove to fresh air. If not breathing, give artificial respiration. If breathing is difficult, give oxygen. Get medical attention

Skin Contact: Immediately flush skin with plenty of water for at least 15 minutes while removing contaminated clothing and shoes. Wash clothing before reuse. Thoroughly clean shoes before reuse. Get medical attention immediately after administering first aid.

Safety Data Sheet

Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting lower and upper eyelids occasionally. Get medical attention immediately after administering first aid.

Ingestion: Call the nearest poison control center or the National Poison Control Hotline at 1-800-222-1222 (U.S.A.), or 703-527-3887 (ChemTrec, collect calls accepted) for advice immediately. Do not induce vomiting, unless directed to do so by a physician. If victim is conscious and alert, give 2-3 glasses of water to drink. Do not leave victim unattended. To prevent aspiration of swallowed product, lay victim on side with head lower than waist. Vomiting may occur spontaneously.

5. FIREFIGHTING MEASURES

This product is not a fire hazard.

Explosion: May cause fire and explosions when in contact with incompatible materials.

Fire Extinguishing Media: Use any means suitable for extinguishing surrounding fire.

Special Information: In the event of a fire, wear full protective clothing and NIOSH-approved self-contained breathing apparatus with full facepiece operated in the pressure demand or other positive pressure mode.

6. SPILL/ACCIDENTAL RELEASE MEASURES

Note: No cleanup should be attempted until cleanup personnel are equipped with personnel protective gear to prevent contact with product. (Applies to undiluted product.)

Remove contaminated clothing immediately. Ventilate area of leak or spill. Keep unnecessary and unprotected people away from area of spill. Wear appropriate personal protective equipment as specified in Section 8.

Spills: Neutralize with sodium bicarbonate, soda ash, or lime. Pick up neutralized solution with a plastic pump or vacuum truck and store the neutralized solution in a leak-proof polyethylene container until product can be disposed of in a hazardous waste facility. Flush area twice with water to remove any remaining residues. Store wash solution in polyethylene containers for disposal. Do not use aluminum tools to collect absorbed material or aluminum containers to store collected wastes. US Regulations (CERCLA) require reporting spills and releases to soil, water and air in excess of reportable quantities. The toll free number for the US Coast Guard National Response Center is (800) 424-8802.

7. HANDLING AND STORAGE

Keep containers closed when not in use. Practice good housekeeping. Wash hands after handling. Avoid smoking when using this product. Wash contaminated clothing before re-use. Keep out of reach of children. Read the disposal information before disposing of leaking or empty containers. Avoid breathing mists or spray. Avoid  contact with eyes. Use only with adequate ventilation. Do not use metal measuring containers for handling this product. Make sure all safety equipment is available and protective clothing is in use before handling this product.

Do not store with aluminum or magnesium containers. Do not mix with acids or organic materials. Keep this and all chemicals out of the reach of children. Wash exposed areas thoroughly after handling.

8. EXPOSURE CONTROLS /PERSONAL PROTECTION

Do not use this product without skin and eye protection.

Do not use this product until you have read all warning statements on bottle and consulted the Safety Data Sheet

Do not use this product unless a source of running water is available.

Wash exposed areas thoroughly after use.

Airborne Exposure Limits:

OSHA Permissible Exposure Limit (PEL): None established

Ventilation System:

A system of local and/or general exhaust is recommended to keep employee exposures below the Airborne Exposure Limits. Local exhaust ventilation is generally preferred because it can control the emissions of the contaminant at its source, preventing dispersion of it into the general work area. Please refer to the ACGIH document, Industrial Ventilation, A Manual of Recommended Practices, most recent edition, for details.

Personal Respirators (NIOSH Approved):

If the exposure limit is exceeded and engineering controls are not feasible, a half facepiece particulate respirator (NIOSH type N95 or better filters or European Standard EN 149 respirators) may be worn for up to ten times the exposure limit or the maximum use concentration specified by the appropriate regulatory agency or respirator supplier, whichever is

Safety Data Sheet

lowest.. A full-face piece particulate respirator (NIOSH type N100 filters) may be worn up to 50 times the exposure limit, or the maximum use concentration specified by the appropriate regulatory agency, or respirator supplier, whichever is lowest. If oil particles (e.g. lubricants, cutting fluids, glycerin, etc.) are present, use a NIOSH type R or P filter with acid-gas cartridge filter. For emergencies or instances where the exposure levels are not known, use a full-face piece positive-pressure, air-supplied respirator. WARNING: Air-purifying respirators do not protect workers in oxygen-deficient atmospheres.

Skin Protection:

Wear impervious protective clothing, including boots, gloves, lab coat, apron or coveralls, as appropriate, to prevent skin contact.

Eye Protection:

Use chemical safety goggles and/or a full face shield where splashing is possible. Maintain eye wash fountain and quick-drench facilities or a source of running water in the work area.

9. PHYSICAL/CHEMICAL CHARACTERISTICS

Boiling Point: >212º F	  	             	Specific gravity (H2O = 1): 1.03

Vapor pressure (mm Hg): Same as water	Melting Point (Pour Point): <32º F

Vapor Density (Air = 1): Same as water 	Evaporation Rate (Water = 1): ~1

Solubility in water: Water miscible		pH, as supplied: 113-11.4

Appearance and odor: Clear liquid with a citrus odor.

10. STABILITY and REACTIVITY DATA

Stability: Stable under ordinary conditions of use and storage.

Compatibility: (Materials to avoid):  Strong acids, strong oxidizers, strong alkalis

Hazardous Decomposition or Byproducts: Hydrogen gas, SO2

Hazardous Polymerization: Will not occur.

Incompatibilities: Do not mix this product with any other material.

Conditions to Avoid: Heat, incompatibles.

11. TOXICOLOGY INFORMATION

RTECS#: Not applicable

Oral Toxicity:Not AVAILABLE

Dermal Toxicity: Not available

CARCINOGENIC EFFECTS: Not available.

MUTAGENIC EFFECTS: Not available.

TERATOGENIC EFFECTS: Not available.

DEVELOPMENTAL TOXICITY: Not available.

The substance may be toxic to blood, liver, skin, eyes, bone marrow.

Repeated or prolonged exposure to the substance can produce target organs damage. Repeated or prolonged contact with spray mist may produce chronic eye irritation and severe skin irritation. Repeated or prolonged exposure to spray mist may produce respiratory tract irritation leading to frequent attacks of bronchial infection. Repeated exposure to a highly toxic material may produce general deterioration of health by an accumulation in one or many human organs

Epidemiology: No information found 
Teratogenicity: No information found 
Reproductive Effects: No information found 
Mutagenicity: No information found 
Neurotoxicity: No information found 
Other Studies:

12. ECOLOGICAL INFORMATION

Ecotoxicity:

No negative effects on the aquatic environment are known.

BOD and COD: Not available

Safety Data Sheet

Biodegradation Products: Possibly hazardous short term degradation products are not likely. However, long term degradation products may arise.

Toxicity of Biodegradation Products: The products of degradation are less toxic than the product itself.

13. DISPOSAL CONSIDERATIONS

Treat empty containers as hazardous. Dispose of spill-clean up and other wastes in accordance with National and local regulations. Whatever cannot be saved for recovery or recycling should be managed in an appropriate and approved waste facility. Although not a listed RCRA hazardous waste, this material may exhibit one or more characteristics of a hazardous waste and require appropriate  analysis to determine specific disposal requirements. Processing, use or contamination of this product may change the waste management options. Dispose of container and unused contents in accordance with federal, state and local requirements.

This product does not contain any prescribed substance under the Environmental Protection Act (Prescribed Processes and Substances) Regulations 1991 and is not classified as special waste under the Control of Substances (Special Waste) Regulations 1996, but is classified as controlled waste under the Environmental Protection Act 1990. For small quantities, dilute with water to at least 2.5% w/v (25 g/litre) and pour down a wastewater drain (foul sewer). Rinse out containers at least twice and recycle if

facilities exist or dispose of as commercial waste. For larger quantities dispose of safely as commercial waste.

European waste catalogue 20 01 29 Detergents containing dangerous substances

14. TRANSPORTATION INFORMATION

ADR: not regulated

US DOT: Not Regulated

International (Water, I.M.O.)

Proper Shipping Name: Not regulated

Hazard Class:  None

UN/NA: None

Packing Group: None

15. REGULATORY INFORMATION

Risk phrases:

Safety phrases

R34: Causes burns

R35: Causes severe burns

R36: Irritating to eyes

R37: Irritating to respiratory system

S1/2: Keep locked up. Keep out of reach of children

S24/25: Avoid contact with skin and eyes

S26: In case of contact with eyes, rinse immediately with plenty of water and seek medical advice.

S 45: In case of accident or if you feel unwell, seek medical advice immediately (show the label  where possible).

US EPA

Comprehensive Environmental Response Compensation and Liability

Act of 1980 (CERCLA) requires notification of the National Response Center of release quantities of Hazardous Substances is not required for this material.

Superfund Amendments and Reauthorization Act of 1986 (SARA) Title III requires emergency planning based on threshold planning quantities and release reporting based on reportable quantities in 40 CFR 355 (used for SARA 302, 304, 311, and 312) is not required for quantities below 250 pounds.

Superfund Amendments and Reauthorization Act of 1986 (SARA) Title III requires submission of annual reports of release of toxic chemicals that appear in 40 CFR 372 (for SARA 313). This material is not subject to reporting requirements.

Toxic Substances Control Act (TSCA) Status: The ingredients of this product are on the TSCA inventory.

Safety Data Sheet

State Right to Know

California Proposition 65:

Massachusetts: Hazardous substances and extraordinarily hazardous substances must be identified.

Pennsylvania: Hazardous substances must be identified.

California SCAQMD Rule 443.1 (VOC’s)

Chemical Inventory Status

Ingredient                                    TSCA EC Japan Australia Korea  DSL NDSL Phil.

Federal, State & International Regulations

SARA 302     SARA 313 TSCA  RCRA

RQ   TPQ

Mixture                                           No    No            No          No          No

SARA 311/312: Acute: No Chronic: No Fire: No Pressure: No Reactivity: No

WHMIS:

This MSDS has been prepared according to the hazard criteria of the Controlled Products Regulations (CPR) and the MSDS contains all of the information required by the CPR.

16. OTHER INFORMATION:

| Indication of changes | Revision 2.0: |
| --- | --- |
| Revision date | 03/30/2016 |

NFPA Ratings: 			Health: 1

Flammability: 0

Reactivity: 0

Label Hazard Warning:

Warning

Label Precautions:

Keep out of reach of children.

Do not use this product without skin and eye protection.

Do not use this product until you have read all warning statements on bottle and consulted the Safety Data Sheet

Do not use this product unless a source of running water is available.

Keep container closed.

Wash thoroughly after use.

Label First Aid:

If swallowed, DO NOT INDUCE VOMITING.  Call a physician immediately. Eyes: flush eyes with running water for at least 15 minutes while lifting lids to rinse the area behind the eyelids. Skin: flush affected area with running water for at least 15 minutes while removing contaminated clothing and shoes. Wash clothing before reuse. If inhaled, remove to fresh air. If breathing does not return to normal within a few minutes, get medical attention.

Product Use:

HVAC Coil Cleaner

Limitations: For sale to and use by trained HVAC professionals only.

This information is based on our current knowledge and is believed to be accurate and reliable as of the date completed. It is intended to describe the product for the purposes of health, safety and environmental requirements only. The information given is designed only as a guidance for safe handling, use, processing, storage, transportation, disposal, and release is not to be considered a warranty or quality specification. Therefore, it should not be construed as guaranteeing any specific property of the product. The user is responsible to ensure safe conditions for handling, storage, and disposal of the product and to assume liability for loss, injury or damage due to improper use.

# Text boxes

Husky Coil Guard

SAFETY DATA SHEET

Prepared according to Federal Register / Vol. 77, No. 58 / March 26, 2012 / Rules and Regulations