|  | Section1. Identification |  |  |  |
| --- | --- | --- | --- | --- |
| Product identifier | HUSKY GREEN FIN COIL CLEANER AEROSOL |
| Other means of identification |  |  |  |
|  |  | Product Code | 11063 110073 604 |  |  |
| Recommended use | Heavy duty grease, oil and carbonized soil remover for HVAC/R components |
| Manufacturer/Importer/Supplier/Distributor information |  |  |
|  | Company name | Bronz-Glow Technologies, Inc. |
|  | Address | 175 Bronz Glow Way |
|  |  |  |  |  | St. Augustine, FL 32095 |
|  |  |  |  |  | United States |
|  | Telephone | 904-825-0175 |
|  | Emergency phone number | Chemtrec 800-424-9300 (US); 703-527-3887 (International) |
|  | Section 2. HAZARD(S) IDENTIFICATION |  |  |
| Physical hazards |  |  |  |
|  |  |  |  |  | Flammable aerosols |  | Category 1 |
|  |  |  |  |  | Gases under pressure | Liquefied gas |
| Health hazards | Serious eye damage/eye irritation | Category 2A |
|  |  |  |  |  | Carcinogenicity |  | Category 2 |
|  |  |  |  |  | Reproductive toxicity |  | Category 2 |
|  |  |  |  |  | Specific target organ toxicity, | Category 3 narcotic effects |
|  |  |  |  |  | single exposure |  | Category 1 |

Specific target organ toxicity, repeated exposure

Environmental hazards

OSHA defined hazards Label elements

Hazardous to the aquatic environment, acute hazard

Hazardous to the aquatic environment, long-term hazard

Not classified.

Category 2

Category 2

Safety Data Sheet

Signal word

Hazard statement

Precautionary statement Prevention

Response

Storage

Disposal

Hazard(s) not otherwise classified (HNOC)

Supplemental information

Danger

Extremely flammable aerosol. Contains gas under pressure; may explode if heated. Causes serious eye irritation. May cause drowsiness or dizziness. Suspected of causing cancer. Suspected of damaging fertility or the unborn child. Causes damage to organs through prolonged or repeated exposure. Toxic to aquatic life. Toxic to aquatic life with long lasting effects.

Obtain special instructions before use. Do not handle until all safety precautions have been read and understood. Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Do not spray on an open flame or other ignition source. Pressurized container: Do not pierce or burn, even after use. Do not breathe mist or vapor. Wash thoroughly after handling. Do not eat, drink or smoke when using this product. Use only outdoors or in a well-ventilated area. Avoid release to the environment. Wear protective gloves/protective clothing/eye protection/face protection.

If inhaled: Remove person to fresh air and keep comfortable for breathing. If in eyes: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. If exposed or concerned: Get medical advice/attention. Call a poison center/doctor if you feel unwell. If eye irritation persists: Get medical advice/attention. Collect spillage.

Store in a well-ventilated place. Keep container tightly closed. Store locked up. Protect from sunlight. Store in a well-ventilated place. Protect from sunlight. Do not expose to temperatures exceeding 50°C/122°F.

Dispose of contents/container in accordance with local/regional/national/international regulations. None known.

23.06% of the mixture consists of component(s) of unknown acute hazards to the aquatic environment. 23.06% of the mixture consists of component(s) of unknown long-term hazards to the aquatic environment.

3. COMPOSITION/INFORMATION ON INGREDIENTS

| Mixtures |  |  |  |
| --- | --- | --- | --- |
| Chemical name | Common name and synonyms | CAS number | % |
| ETHYL ALCOHOL |  | 64-17-5 | 40 to <50 |
| ACETONE |  | 67-64-1 | 30 to <40 |
| PROPANE |  | 74-98-6 | 10 to <20 |
| N-BUTANE |  | 106-97-8 | 5 to <10 |
| METHANOL |  | 67-56-1 | 1 to <5 |
| 4-Methyl-2-pentanone |  | 108-10-1 | 0.1 to <1 |
| HEPTANE |  | 142-82-5 | 0.1 to <1 |
| Other components below reportable levels |  |  | 0.1 to <1 |

*Designates that a specific chemical identity and/or percentage of composition has been withheld as a trade secret.

4. FIRST-AID MEASURES

Inhalation Remove victim to fresh air and keep at rest in a position comfortable for breathing. Call a POISON CENTER or doctor/physician if you feel unwell.

Skin contact No adverse effects due to skin contact are expected. Rinse skin with water/shower. Get medical attention if irritation develops and persists.

Eye contact Immediately flush eyes with plenty of water for at least 15 minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Get medical attention if irritation develops and persists. No specific first aid measures noted.

Safety Data Sheet

Ingestion

Most important symptoms/effects, acute and delayed

Indication of immediate medical attention and special treatment needed

General information

Not likely, due to the form of the product. In the unlikely event of swallowing contact a physician or poison control center. Rinse mouth.

May cause drowsiness and dizziness. Headache. Nausea, vomiting. Severe eye irritation. Symptoms may include stinging, tearing, redness, swelling, and blurred vision. Coughing. Prolonged exposure may cause chronic effects.

Provide general supportive measures and treat symptomatically. Keep victim under observation. Symptoms may be delayed.

IF exposed or concerned: Get medical advice/attention. If you feel unwell, seek medical advice (show the label where possible). Ensure that medical personnel are aware of the material(s) involved, and take precautions to protect themselves. Show this safety data sheet to the doctor in attendance.

5. FIRE-FIGHTING MEASURES

Suitable extinguishing media	Alcohol resistant foam. Water fog. Dry chemical powder. Carbon dioxide (CO2).

Unsuitable extinguishing	Do not use water jet as an extinguisher, as this will spread the fire.

media

Specific hazards arising from	Contents under pressure. Pressurized container may explode when exposed to heat or flame.

the chemical	During fire, gases hazardous to health may be formed.

Special protective equipment	Firefighters must use standard protective equipment including flame retardant coat, helmet with

and precautions for firefighters	face shield, gloves, rubber boots, and in enclosed spaces, SCBA.

Fire fighting	In case of fire: Stop leak if safe to do so. Do not move cargo or vehicle if cargo has been exposed

equipment/instructions	to heat. Move containers from fire area if you can do so without risk. Containers should be cooled

with water to prevent vapor pressure build up. For massive fire in cargo area, use unmanned hose

holder or monitor nozzles, if possible. If not, withdraw and let fire burn out.

Specific methods	Use standard firefighting procedures and consider the hazards of other involved materials. Move

containers from fire area if you can do so without risk. In the event of fire and/or explosion do not

breathe fumes.

General fire hazards	Extremely flammable aerosol. Contents under pressure. Pressurized container may explode when

exposed to heat or flame.

6. ACCIDENTAL RELEASE MEASURES

Personal precautions, protective equipment and emergency procedures

Methods and materials for containment and cleaning up

Environmental precautions

Keep unnecessary personnel away. Keep people away from and upwind of spill/leak. Keep out of low areas. Many gases are heavier than air and will spread along ground and collect in low or confined areas (sewers, basements, tanks). Wear appropriate protective equipment and clothing during clean-up. Do not breathe mist or vapor. Emergency personnel need self-contained breathing equipment. Do not touch damaged containers or spilled material unless wearing appropriate protective clothing. Ventilate closed spaces before entering them. Local authorities should be advised if significant spillages cannot be contained. For personal protection, see section 8 of the SDS.

Refer to attached safety data sheets and/or instructions for use. Eliminate all ignition sources (no smoking, flares, sparks, or flames in immediate area). Keep combustibles (wood, paper, oil, etc.) away from spilled material. Stop leak if you can do so without risk. Move the cylinder to a safe and open area if the leak is irreparable. Isolate area until gas has dispersed. Cover with plastic sheet to prevent spreading. Absorb in vermiculite, dry sand or earth and place into containers. Prevent entry into waterways, sewer, basements or confined areas. Following product recovery, flush area with water.

Small Spills: Wipe up with absorbent material (e.g. cloth, fleece). Clean surface thoroughly to remove residual contamination. For waste disposal, see section 13 of the SDS.

Avoid release to the environment. Prevent further leakage or spillage if safe to do so. Avoid discharge into drains, water courses or onto the ground. Inform appropriate managerial or supervisory personnel of all environmental releases.

Safety Data Sheet

7. HANDLING AND STORAGE

| Precautions for safe handling | Obtain special instructions before use. Do not handle until all safety precautions have been read |
| --- | --- |
|  | and understood. Pressurized container: Do not pierce or burn, even after use. Do not use if spray |
|  | button is missing or defective. Do not spray on a naked flame or any other incandescent material. |
|  | Do not smoke while using or until sprayed surface is thoroughly dry. Do not cut, weld, solder, drill, |
|  | grind, or expose containers to heat, flame, sparks, or other sources of ignition. All equipment used |
|  | when handling the product must be grounded. Do not re-use empty containers. Do not breathe |
|  | mist or vapor. Avoid contact with eyes. Avoid prolonged exposure. When using, do not eat, drink |
|  | or smoke. Pregnant or breastfeeding women must not handle this product. Should be handled in |
|  | closed systems, if possible. Use only in well-ventilated areas. Wear appropriate personal |
|  | protective equipment. Wash hands thoroughly after handling. Avoid release to the environment. |
|  | Observe good industrial hygiene practices. |
| Conditions for safe storage, | Level 2 Aerosol. |
| including any incompatibilities |  |
|  | Store locked up. Pressurized container. Protect from sunlight and do not expose to temperatures |
|  | exceeding 50°C/122 °F. Do not puncture, incinerate or crush. Do not handle or store near an open |
|  | flame, heat or other sources of ignition. This material can accumulate static charge which may |
|  | cause spark and become an ignition source. Secure cylinders in an upright position at all times. |
|  | Store in a well-ventilated place. Store away from incompatible |
|  | materials (see Section 10 of the SDS). |

8. EXPOSURE CONTROLS/PERSONAL

PROTECTION

| Occupational exposure limits |  | Value |
| --- | --- | --- |
|  | US. OSHA Table Z-1 Limits for Air Contaminants (29 CFR 1910.1000) |  |
|  | Components | Type |  |
|  | 4-Methyl-2-pentanone (CAS | PEL | 410 mg/m3 |
| 108-10-1) |  |  |
|  |  |  | 100 ppm |
|  | ACETONE (CAS 67-64-1) | PEL | 2400 mg/m3 |
|  |  |  | 1000 ppm |
|  | ETHYL ALCOHOL (CAS | PEL | 1900 mg/m3 |
| 64-17-5) |  |  |

Safety Data Sheet

| US. OSHA Table Z-1 Limits for Air Contaminants (29 CFR 1910.1000) |  |  |
| --- | --- | --- |
| Components | Type |  |  | Value |
|  |  |  |  | 1000 ppm |
| HEPTANE (CAS 142-82-5) | PEL |  |  | 2000 mg/m3 |
|  |  |  |  | 500 ppm |
| METHANOL (CAS 67-56-1) | PEL |  |  | 260 mg/m3 |
| PROPANE (CAS 74-98-6) |  |  |  | 200 ppm |
|  | PEL |  |  | 1800 mg/m3 |
|  |  |  |  | 1000 ppm |
| US. ACGIH Threshold Limit Values |  |  |  |
| Components | Type |  |  | Value |
| 4-Methyl-2-pentanone (CAS | STEL |  |  | 75 ppm |
| 108-10-1) |  |  |  |  |
|  | TWA |  |  | 20 ppm |
| ACETONE (CAS 67-64-1) | STEL |  |  | 750 ppm |
|  | TWA |  |  | 500 ppm |
| ETHYL ALCOHOL (CAS | STEL |  |  | 1000 ppm |
| 64-17-5) |  |  |  |  |
| HEPTANE (CAS 142-82-5) | STEL |  |  | 500 ppm |
|  | TWA |  |  | 400 ppm |
| METHANOL (CAS 67-56-1) | STEL |  |  | 250 ppm |
| N-BUTANE (CAS 106-97-8) | TWA |  |  | 200 ppm |
|  | STEL |  |  | 1000 ppm |
| US. NIOSH: Pocket Guide to Chemical Hazards |  |  |  |
| Components | Type |  |  | Value |
| 4-Methyl-2-pentanone (CAS | STEL |  |  | 300 mg/m3 |
| 108-10-1) |  |  |  |  |
|  |  |  |  | 75 ppm |
|  | TWA |  |  | 205 mg/m3 |
|  |  |  |  | 50 ppm |
| ACETONE (CAS 67-64-1) | TWA |  |  | 590 mg/m3 |
| ETHYL ALCOHOL (CAS |  |  |  | 250 ppm |
|  | TWA |  |  | 1900 mg/m3 |
| 64-17-5) |  |  |  |  |
| HEPTANE (CAS 142-82-5) |  |  |  | 1000 ppm |
|  | Ceiling |  |  | 1800 mg/m3 |
|  |  |  |  | 440 ppm |
|  | TWA |  |  | 350 mg/m3 |
| METHANOL (CAS 67-56-1) |  |  |  | 85 ppm |
|  | STEL |  |  | 325 mg/m3 |
|  |  |  |  | 250 ppm |
|  | TWA |  |  | 260 mg/m3 |
| N-BUTANE (CAS 106-97-8) |  |  |  | 200 ppm |
|  | TWA |  |  | 1900 mg/m3 |
| PROPANE (CAS 74-98-6) |  |  |  | 800 ppm |
|  | TWA |  |  | 1800 mg/m3 |
| Biological limit values |  |  |  | 1000 ppm |
| ACGIH Biological Exposure Indices |  |  |  |
| Components | Value | Determinant | Specimen | Sampling Time |
| 4-Methyl-2-pentanone (CAS 1 mg/l | Methyl isobutyl | Urine | * |
| 108-10-1) |  | ketone |  |  |
| ACETONE (CAS 67-64-1) | 50 mg/l | Acetone | Urine | * |
| METHANOL (CAS 67-56-1) 15 mg/l | Methanol | Urine | * |

* - For sampling details, please see the source document.

Safety Data Sheet

Exposure guidelines

US - California OELs: Skin designation

METHANOL (CAS 67-56-1)	Can be absorbed through the skin.

US - Minnesota Haz Subs: Skin designation applies

METHANOL (CAS 67-56-1)	Skin designation applies.

US - Tennessee OELs: Skin designation

METHANOL (CAS 67-56-1)	Can be absorbed through the skin.

US ACGIH Threshold Limit Values: Skin designation

METHANOL (CAS 67-56-1)	Can be absorbed through the skin.

US NIOSH Pocket Guide to Chemical Hazards: Skin designation

METHANOL (CAS 67-56-1)	Can be absorbed through the skin.

Appropriate engineering              Good general ventilation (typically 10 air changes per hour) should be used. Ventilation rates

Controls                                         should be matched to conditions. If applicable, use process enclosures, local exhaust ventilation,

or other engineering controls to maintain airborne levels below recommended exposure limits. If

exposure limits have not been established, maintain airborne levels to an acceptable level. Provide

eyewash station.

Individual protection measures, such as personal protective	equipment

Eye/face protection	Wear safety glasses with side shields (or goggles).

Skin protection Hand protection

Other Respiratory protection Thermal hazards

General hygiene considerations

For prolonged or repeated skin contact use suitable protective gloves.

Wear suitable protective clothing.

In case of insufficient ventilation, wear suitable respiratory equipment.

Wear appropriate thermal protective clothing, when necessary.

When using do not smoke. Always observe good personal hygiene measures, such as washing after handling the material and before eating, drinking, and/or smoking. Routinely wash work clothing and protective equipment to remove contaminants.

9. PHYSICAL AND CHEMICAL PROPERTIES

Appearance

Physical state	Liquid.

Form	Aerosol. Liquefied gas.

Color	Not available.

Odor	Not available.

Odor threshold	Not available.

pH	Not available.

Melting point/freezing point	-305.68 °F (-187.6 °C) estimated

Initial boiling point and boiling	-43.78 °F (-42.1 °C) estimated

range

Flash point	-156.0 °F (-104.4 °C) estimated

Evaporation rate	Not available.

Flammability (solid, gas)	Not applicable.

Upper/lower flammability or explosive limits

Flammability limit - lower	1.9 % estimated

(%)

Flammability limit - upper	12.8 % estimated

(%)

Explosive limit - lower (%)	Not available.

Explosive limit - upper (%)	Not available.

Vapor pressure	1634.68 hPa estimated

Safety Data Sheet

| Vapor density | Not available. |
| --- | --- |
| Relative density | Not available. |
| Solubility(ies) |  |
| Solubility (water) | Not available. |
| Partition coefficient | Not available. |
| (n-octanol/water) |  |
| Auto-ignition temperature | 550 °F (287.78 °C) estimated |
| Decomposition temperature | Not available. |
| Viscosity | Not available. |
| Other information |  |
| Density | 6.00 lbs/gal |
| Flammability class | Flammable IA estimated |
| Heat of combustion (NFPA | 29.33 kJ/g estimated |
| 30B) |  |
| Percent volatile | 100 |
| Specific gravity | 0.72 |
| VOC | 488.664703 g/l Material |
|  | 5.7649177 lbs/gal Regulatory |
|  | 690.78949 g/l Regulatory |
|  | 4.0781046 lbs/gal Material |

10.  STABILITY AND REACTIVITY

Reactivity Chemical stability

Possibility of hazardous reactions

Conditions to avoid Incompatible materials

Hazardous decomposition products

The product is stable and non-reactive under normal conditions of use, storage and transport. Material is stable under normal conditions.

No dangerous reaction known under conditions of normal use.

Heat. Avoid temperatures exceeding the flash point. Contact with incompatible materials. Acids. Strong oxidizing agents. Nitrates. Fluorine. Chlorine.

No hazardous decomposition products are known.

11.  TOXICOLOGICAL INFORMATION

Information on likely routes of exposure

Inhalation	May cause damage to organs through prolonged or repeated exposure by inhalation. May cause

drowsiness and dizziness. Headache. Nausea, vomiting. Prolonged inhalation may be harmful.

Skin contact Eye contact Ingestion

Symptoms related to the physical, chemical and toxicological characteristics

No adverse effects due to skin contact are expected. Causes serious eye irritation.

Expected to be a low ingestion hazard.

Headache. May cause drowsiness and dizziness. Nausea, vomiting. Severe eye irritation. Symptoms may include stinging, tearing, redness, swelling, and blurred vision. Coughing.

Safety Data Sheet

| Information on toxicological effects |  |  |
| --- | --- | --- |
| Acute toxicity | Narcotic effects. |  |
| Components |  | Species | Test Results |
| 4-Methyl-2-pentanone (CAS 108-10-1) |  |
| Acute |  |  |  |
| Dermal |  |  |  |
| LD50 |  | Rabbit | > 16000 mg/kg |
| Inhalation |  |  |  |
| LC50 |  | Rat | 8.2 mg/l, 4 Hours |
| Oral |  |  |  |
| LD50 |  | Rat | 2080 mg/kg |
| ACETONE (CAS 67-64-1) |  |  |  |
| Acute |  |  |  |
| Dermal |  |  |  |
| LD50 |  | Rabbit | > 15800 mg/kg |
| Components |  | Species | Test Results |
| Inhalation |  |  |  |
| LC50 |  | Rat | 76 mg/l, 4 Hours |
| Oral |  |  |  |
| LD50 |  | Mouse | 3000 mg/kg |
|  |  | Rat | 5800 mg/kg |
| ETHYL ALCOHOL (CAS 64-17-5) |  |  |  |
| Acute |  |  |  |
| Inhalation |  |  |  |
| LC50 |  | Mouse | 39 mg/l, 4 Hours |
|  |  | Rat | 20000 ppm, 10 Hours |
| Oral |  |  |  |
| LD50 |  | Guinea pig | 5.6 g/kg |
|  |  | Mouse | 3450 mg/kg |
|  |  | Rat | 6.2 g/kg |
| HEPTANE (CAS 142-82-5) |  |  |  |
| Acute |  |  |  |
| Inhalation |  |  |  |
| LC50 |  | Rat | 103 mg/l, 4 Hours |
| LD50 |  | Mouse | 75 mg/l, 2 Hours |
| METHANOL (CAS 67-56-1) |  |  |  |
| Acute |  |  |  |
| Dermal |  |  |  |
| LD50 |  | Rabbit | 15800 mg/kg |
| Inhalation |  |  |  |
| LC50 |  | Rat | 64000 ppm, 4 Hours |
|  |  |  | 87.5 mg/l, 6 Hours |
|  | Issue date: 9-21-2015 |  |

Respiratory or skin sensitization Respiratory sensitization Skin sensitization

Germ cell mutagenicity Carcinogenicity

Serious eye damage/eye irritation

Skin corrosion/irritation

Safety Data Sheet

| Oral |  |  |
| --- | --- | --- |
| LD50 | Monkey | 2 g/kg |
|  | Mouse | 7300 mg/kg |
|  | Rabbit | 14.4 g/kg |
|  | Rat | 5628 mg/kg |
| N-BUTANE (CAS 106-97-8) |  |  |
| Acute |  |  |
| Inhalation |  |  |
| LC50 | Mouse | 680 mg/l, 2 Hours |
|  | Rat | 658 mg/l, 4 Hours |
| PROPANE (CAS 74-98-6) |  |  |
| Acute |  |  |
| Inhalation |  |  |
| LC50 | Rat | > 1442.847 mg/l, 15 Minutes |

* Estimates for product may be based on additional component data not shown.

Prolonged skin contact may cause temporary irritation. Causes serious eye irritation.

Not a respiratory sensitizer.

This product is not expected to cause skin sensitization.

No data available to indicate product or any components present at greater than 0.1% are mutagenic or genotoxic.

Suspected of causing cancer.

IARC Monographs. Overall Evaluation of Carcinogenicity

4-Methyl-2-pentanone (CAS 108-10-1)	2B Possibly carcinogenic to humans.

OSHA Specifically Regulated Substances (29 CFR 1910.1001-1050)

Not listed.

Reproductive toxicity	Suspected of damaging fertility or the unborn child.

Specific target organ toxicity -	May cause drowsiness and dizziness.

single exposure

Specific target organ toxicity -	Causes damage to organs through prolonged or repeated exposure.

repeated exposure

Aspiration hazard	Not an aspiration hazard.

Chronic effects	Causes damage to organs through prolonged or repeated exposure. Prolonged inhalation may be

harmful. Prolonged exposure may cause chronic effects.

Safety Data Sheet

12.  ECOLOGICAL INFORMATION

| Ecotoxicity | Toxic to aquatic life with long lasting effects. |  |
| --- | --- | --- |
|  | Components |  | Species | Test Results |
|  | 4-Methyl-2-pentanone (CAS 108-10-1) |  |  |
|  | Aquatic |  |  |  |
|  | Fish | LC50 | Fathead minnow (Pimephales promelas) | 492 - 593 mg/l, 96 hours |
|  | ACETONE (CAS 67-64-1) |  |  |
|  | Aquatic |  |  |  |
|  | Crustacea | EC50 | Water flea (Daphnia magna) | 21.6 - 23.9 mg/l, 48 hours |
|  | Fish | LC50 | Rainbow trout,donaldson trout | 4740 - 6330 mg/l, 96 hours |
|  |  |  | (Oncorhynchus mykiss) |  |
|  | ETHYL ALCOHOL (CAS 64-17-5) |  |  |
|  | Aquatic |  |  |  |
|  | Crustacea | EC50 | Water flea (Daphnia magna) | 7.7 - 11.2 mg/l, 48 hours |
|  | Fish | LC50 | Fathead minnow (Pimephales promelas) | > 100 mg/l, 96 hours |
|  | HEPTANE (CAS 142-82-5) |  |  |
|  | Aquatic |  |  |  |
|  | Fish | LC50 | Mozambique tilapia (Tilapia | 375 mg/l, 96 hours |
|  |  |  | mossambica) |  |
|  | METHANOL (CAS 67-56-1) |  |  |
|  | Aquatic |  |  |  |
|  | Crustacea | EC50 | Water flea (Daphnia magna) | > 10000 mg/l, 48 hours |
|  | Fish | LC50 | Fathead minnow (Pimephales promelas) | > 100 mg/l, 96 hours |

* Estimates for product may be based on additional component data not shown. Persistence and degradability No data is available on the degradability of this product.

Bioaccumulative potential

Partition coefficient n-octanol / water (log Kow)

| 4-Methyl-2-pentanone | 1.31 |
| --- | --- |
| ACETONE | -0.24 |
| ETHYL ALCOHOL | -0.31 |
| HEPTANE | 4.66 |
| METHANOL | -0.77 |
| N-BUTANE | 2.89 |
| PROPANE | 2.36 |
| Mobility in soil | No data available. |
| Other adverse effects | No other adverse environmental effects (e.g. ozone depletion, photochemical ozone creation |
|  | potential, endocrine disruption, global warming potential) are expected from this component. |

Collect and reclaim or dispose in sealed containers at licensed waste disposal site. Contents under pressure. Do not puncture, incinerate or crush. Do not allow this material to drain into sewers/water supplies. Do not contaminate ponds, waterways or ditches with chemical or used container. Dispose of contents/container in accordance with local/regional/national/international regulations.

The waste code should be assigned in discussion between the user, the producer and the waste disposal company.

Dispose of in accordance with local regulations. Empty containers or liners may retain some product residues. This material and its container must be disposed of in a safe manner (see: Disposal instructions).

Since emptied containers may retain product residue, follow label warnings even after container is emptied. Empty containers should be taken to an approved waste handling site for recycling or disposal. Do not re-use empty containers.

UN1950

Aerosols, Flammable

-

2.1

Not applicable.

Safety Data Sheet

13.  DISPOSAL CONSIDERATIONS

Disposal instructions

Dispose in accordance with all applicable regulations.

Local disposal regulations

Hazardous waste code

Waste from residues / unused products

Contaminated packaging

14.  TRANSPORT

INFORMATION

DOT

UN number

2.1

UN proper shipping name Transport hazard class(es)

Class Subsidiary risk Label(s)

Packing group

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

Special provisions	N82

Packaging exceptions	306

Packaging non bulk	None

Packaging bulk	None

IATA

UN number	UN1950

UN proper shipping name	Aerosols, Flammable

Transport hazard class(es)

Class	2.1

Subsidiary risk	-

Label(s)	2.1

Packing group	Not applicable.

Environmental hazards	No.

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

Other information

Passenger and cargo	Allowed

aircraft

Cargo aircraft only	Allowed

Safety Data Sheet

IMDG

UN number	UN1950

UN proper shipping name	Aerosols, Flammable,

Transport hazard class(es)

Class	2.1

Subsidiary risk	-

Label(s)	2.1

Packing group	Not applicable.

Environmental hazards

Marine pollutant	Not applicable.

EmS	Not available.

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

Transport in bulk according to	Not established.

Annex II of MARPOL 73/78 and

the IBC Code

DOT

IATA; IMDG

General information

Avoid transport on vehicles where the load space is not separated from the driver's compartment. Ensure vehicle driver is aware of the potential hazards of the load and knows what to do in the event of an accident or an emergency. Before transporting product containers: Ensure that containers are firmly secured.  Ensure valve outlet cap nut or plug (where provided) is correctly fitted. Ensure adequate ventilation. Ensure compliance with applicable regulations

Safety Data Sheet

15.  REGULATORY INFORMATION

| US federal regulations | This product is a "Hazardous Chemical" as defined by the OSHA Hazard Communication |
| --- | --- |
|  |  | Standard, 29 CFR 1910.1200. |  |  |  |
|  |  | All components are on the U.S. EPA TSCA Inventory List. |
| TSCA Section 12(b) Export Notification (40 CFR 707, Subpt. D) |  |  |
|  | Not regulated. |  |  |  |  |
| CERCLA Hazardous Substance List (40 CFR 302.4) |  |  |  |
|  | 4-Methyl-2-pentanone (CAS 108-10-1) | Listed. |  |  |
|  | ACETONE (CAS 67-64-1) |  | Listed. |  |  |
|  | ETHYL ALCOHOL (CAS 64-17-5) | Listed. |  |  |
|  | HEPTANE (CAS 142-82-5) |  | Listed. |  |  |
|  | METHANOL (CAS 67-56-1) | Listed. |  |  |
|  | N-BUTANE (CAS 106-97-8) | Listed. |  |  |
|  | PROPANE (CAS 74-98-6) |  | Listed. |  |  |
| SARA 304 Emergency release notification |  |  |  |
|  | Not regulated. |  |  |  |  |
| OSHA Specifically Regulated Substances (29 CFR 1910.1001-1050) |  |  |
|  | Not listed. |  |  |  |  |
| Superfund Amendments and Reauthorization Act of 1986 (SARA) |  |  |
| Hazard categories | Immediate Hazard - Yes |  |  |  |
|  |  | Delayed Hazard - Yes |  |  |  |
|  |  | Fire Hazard - Yes |  |  |  |
|  |  | Pressure Hazard - No |  |  |  |
|  |  | Reactivity Hazard - No |  |  |  |
|  | SARA 302 Extremely hazardous substance |  |  |  |
|  | Not listed. |  |  |  |  |
| SARA 311/312 Hazardous | No |  |  |  |
| chemical |  |  |  |  |
| SARA 313 (TRI reporting) |  |  |  |  |
|  | Chemical name |  | CAS number | % by wt. |
|  | METHANOL |  | 67-56-1 | 1 to <5 |
|  | 4-Methyl-2-pentanone |  | 108-10-1 | 0.1 to <1 |
| Other federal regulations |  |  |  |  |

Clean Air Act (CAA) Section 112 Hazardous Air Pollutants (HAPs) List

4-Methyl-2-pentanone (CAS 108-10-1) METHANOL (CAS 67-56-1)

Clean Air Act (CAA) Section 112(r) Accidental Release Prevention (40 CFR 68.130)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

Safe Drinking Water Act	Not regulated.

(SDWA)

Safety Data Sheet

Drug Enforcement Administration (DEA). List 2, Essential Chemicals (21 CFR 1310.02(b) and 1310.04(f)(2) and Chemical Code Number

| 4-Methyl-2-pentanone (CAS 108-10-1) | 6715 |
| --- | --- |
| ACETONE (CAS 67-64-1) | 6532 |
| Drug Enforcement Administration (DEA). List 1 & 2 Exempt Chemical Mixtures (21 CFR 1310.12(c)) |
| 4-Methyl-2-pentanone (CAS 108-10-1) | 35 %WV |
| ACETONE (CAS 67-64-1) | 35 %WV |
| DEA Exempt Chemical Mixtures Code Number |  |
| 4-Methyl-2-pentanone (CAS 108-10-1) | 6715 |
| ACETONE (CAS 67-64-1) | 6532 |

US state regulations

US. California Controlled Substances. CA Department of Justice (California Health and Safety Code Section 11100)

Not listed.

US. California. Candidate Chemicals List. Safer Consumer Products Regulations (Cal. Code Regs, tit. 22, 69502.3, subd. (a))

4-Methyl-2-pentanone (CAS 108-10-1) ACETONE (CAS 67-64-1) METHANOL (CAS 67-56-1) N-BUTANE (CAS 106-97-8)

US. Massachusetts RTK - Substance List

4-Methyl-2-pentanone (CAS 108-10-1) ACETONE (CAS 67-64-1)

ETHYL ALCOHOL (CAS 64-17-5) HEPTANE (CAS 142-82-5) METHANOL (CAS 67-56-1) N-BUTANE (CAS 106-97-8) PROPANE (CAS 74-98-6)

US. New Jersey Worker and Community Right-to-Know Act

4-Methyl-2-pentanone (CAS 108-10-1) ACETONE (CAS 67-64-1)

ETHYL ALCOHOL (CAS 64-17-5) HEPTANE (CAS 142-82-5) METHANOL (CAS 67-56-1) N-BUTANE (CAS 106-97-8) PROPANE (CAS 74-98-6)

US. Pennsylvania Worker and Community Right-to-Know Law

4-Methyl-2-pentanone (CAS 108-10-1) ACETONE (CAS 67-64-1)

ETHYL ALCOHOL (CAS 64-17-5) HEPTANE (CAS 142-82-5) METHANOL (CAS 67-56-1) N-BUTANE (CAS 106-97-8) PROPANE (CAS 74-98-6)

US. Rhode Island RTK

4-Methyl-2-pentanone (CAS 108-10-1)

ACETONE (CAS 67-64-1)

METHANOL (CAS 67-56-1)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

US. California Proposition 65

WARNING: This product contains a chemical known to the State of California to cause cancer and birth defects or other reproductive harm.

Safety Data Sheet

US - California Proposition 65 - CRT: Listed date/Carcinogenic substance

4-Methyl-2-pentanone (CAS 108-10-1)	Listed: November 4, 2011

ETHYL ALCOHOL (CAS 64-17-5)	Listed: April 29, 2011

Listed: July 1, 1988

US - California Proposition 65 - CRT: Listed date/Developmental toxin

4-Methyl-2-pentanone (CAS 108-10-1)	Listed: March 28, 2014

ETHYL ALCOHOL (CAS 64-17-5)	Listed: October 1, 1987

METHANOL (CAS 67-56-1)	Listed: March 16, 2012

| International Inventories |  |  |
| --- | --- | --- |
| Country(s) or region | Inventory name | On inventory (yes/no)* |
| Australia | Australian Inventory of Chemical Substances (AICS) | Yes |
| Canada | Domestic Substances List (DSL) | Yes |
| Canada | Non-Domestic Substances List (NDSL) | No |
| China | Inventory of Existing Chemical Substances in China (IECSC) | Yes |
| Europe | European Inventory of Existing Commercial Chemical | Yes |
|  | Substances (EINECS) |  |

Europe	European List of Notified Chemical Substances (ELINCS)

Japan	Inventory of Existing and New Chemical Substances (ENCS)

Korea	Existing Chemicals List (ECL)

New Zealand	New Zealand Inventory

Philippines	Philippine Inventory of Chemicals and Chemical Substances

(PICCS)

No

Yes

Yes

Yes

Yes

United States & Puerto Rico	Toxic Substances Control Act (TSCA) Inventory	Yes

*A "Yes" indicates that all components of this product comply with the inventory requirements administered by the governing country(s)

A "No" indicates that one or more components of the product are not listed or exempt from listing on the inventory administered by the governing country(s).

16.  OTHER INFORMATION, INCLUDING DATE OF PREPARATION OR LAST

REVISION

| Issue date | 08-12-2015 |
| --- | --- |
| Revision date | 06-30-2016 |
| Version # | 05 |
| HMIS® ratings | Health: 2* |
|  | Flammability: 4 |
|  | Physical hazard: 0 |
| NFPA ratings | Health: 2 |
|  | Flammability: 4 |
|  | Instability: 0 |
| Disclaimer |  |
|  | This information is based on our current knowledge and is believed to be accurate and reliable as of the date completed. It is intended to describe the product for the purposes of health, safety and environmental requirements only. The information given is designed only as a guidance for safe handling, use, processing, storage, transportation, disposal, and release is not to be considered a warranty or quality specification. Therefore, it should not be construed as guaranteeing any specific property of the product. The user is responsible to ensure safe conditions for handling, storage, and disposal of the product and to assume liability for loss, injury or damage due to improper use. |

# Text boxes

HUSKY GREEN FIN COIL CLEANER AEROSOL

Safety Data Sheet

Prepared according to Federal Register / Vol. 77, No. 58 /  March 26, 2012 / Rules and Regulations