|  | 1. IDENTIFICATION |  |
| --- | --- | --- |
| Product identifier | HUSKY GREEN FIN PRIMER AEROSOL |
| Other means of identification |  |

| Product Code | 11063 110074 604 |
| --- | --- |
| Recommended use | Para la adherencia de la capa de mayor |

Manufacturer/Importer/Supplier/Distributor information Manufacturer

Company name

Address

Telephone

Emergency phone number

Bronz-Glow Technologies, Inc.

175 Bronz-Glow Way

St. Augustine, FL 32095 United States

904-825-0175

Chemtrec Phone   800-424-9300

(US)      703-527-3887 (International)

2. HAZARD(S)

IDENTIFICATION

Physical hazards

Health hazards

Environmental hazards

OSHA defined hazards Label elements

Flammable aerosols

Gases under pressure

Acute toxicity, dermal Skin corrosion/irritation

Serious eye damage/eye irritation Carcinogenicity

Reproductive toxicity

Specific target organ toxicity, single exposure

Specific target organ toxicity, repeated exposure

Hazardous to the aquatic environment, acute hazard

Hazardous to the aquatic environment, long-term hazard

Not classified.

Category 1

Liquefied gas

Category 4

Category 2

Category 2B

Category 2

Category 2

Category 3

narcotic effects

Category 1

Category 2

Category 2

Signal word			Danger

Safety Data Sheet

Hazard statement

Precautionary statement Prevention

Response

Storage

Disposal

Hazard(s) not otherwise classified (HNOC)

Supplemental information

Extremely flammable aerosol. Contains gas under pressure; may explode if heated. Harmful in contact with skin. Causes skin irritation. Causes eye irritation. May cause drowsiness or dizziness. Suspected of causing cancer. Suspected of damaging fertility or the unborn child. Causes damage to organs through prolonged or repeated exposure. Toxic to aquatic life. Toxic to aquatic life with long lasting effects.

Obtain special instructions before use. Do not handle until all safety precautions have been read and understood. Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Do not spray on an open flame or other ignition source. Pressurized container: Do not pierce or burn, even after use. Do not breathe mist or vapor. Wash thoroughly after handling. Do not eat, drink or smoke when using this product. Use only outdoors or in a well-ventilated area. Avoid release to the environment. Wear protective gloves/protective clothing/eye protection/face protection.

If on skin: Wash with plenty of water. If inhaled: Remove person to fresh air and keep comfortable for breathing. If in eyes: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. If exposed or concerned: Get medical advice/attention. Call a poison center/doctor if you feel unwell. If skin irritation occurs: Get medical advice/attention. If eye irritation persists: Get medical advice/attention. Take off contaminated clothing and wash before reuse. Collect spillage.

Store in a well-ventilated place. Keep container tightly closed. Store locked up. Protect from sunlight. Store in a well-ventilated place. Protect from sunlight. Do not expose to temperatures exceeding 50°C/122°F.

Dispose of contents/container in accordance with local/regional/national/international regulations.

None known.

94.45% of the mixture consists of component(s) of unknown acute dermal toxicity. 70.1% of the mixture consists of component(s) of unknown acute hazards to the aquatic environment. 70.1% of the mixture consists of component(s) of unknown long-term hazards to the aquatic environment.

3. COMPOSITION/INFORMATION ON

INGREDIENTS

| Mixtures |  |  |  |
| --- | --- | --- | --- |
| Chemical name | Common name and synonyms | CAS number | % |
| DIMETHYL ETHER |  | 115-10-6 | 50 to <60 |
| HEPTANE |  | 142-82-5 | 20 to <30 |
| ETHYLBENZENE |  | 100-41-4 | 1 to <5 |
| XYLENE |  | 1330-20-7 | 1 to <5 |
| Other components below reportable levels |  |  | 20 to <30 |

*Designates that a specific chemical identity and/or percentage of composition has been withheld as a trade secret.

Safety Data Sheet

4. FIRST-AID MEASURES

Inhalation

Skin contact

Eye contact

Ingestion

Most important symptoms/effects, acute and delayed

Indication of immediate medical attention and special treatment needed

General information

Remove victim to fresh air and keep at rest in a position comfortable for breathing. Call a POISON CENTER or doctor/physician if you feel unwell.

No adverse effects due to skin contact are expected. Remove contaminated clothing. Rinse skin with water/shower. Get medical advice/attention if you feel unwell. If skin irritation occurs: Get medical advice/attention. Wash contaminated clothing before reuse.

Immediately flush eyes with plenty of water for at least 15 minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Get medical attention if irritation develops and persists. No specific first aid measures noted.

Not likely, due to the form of the product. Rinse mouth. Get medical advice/attention if you feel unwell.

May cause drowsiness and dizziness. Headache. Nausea, vomiting. Irritation of eyes. Exposed individuals may experience eye tearing, redness, and discomfort. Skin irritation. May cause redness and pain. Prolonged exposure may cause chronic effects.

Provide general supportive measures and treat symptomatically. Keep victim warm. Keep victim under observation. Symptoms may be delayed.

IF exposed or concerned: Get medical advice/attention. If you feel unwell, seek medical advice (show the label where possible). Ensure that medical personnel are aware of the material(s) involved, and take precautions to protect themselves. Show this safety data sheet to the doctor in attendance.

5. FIRE-FIGHTING MEASURES

Suitable extinguishing media	Water fog. Foam. Dry chemical powder. Carbon dioxide (CO2).

Unsuitable extinguishing media	Do not use water jet as an extinguisher, as this will spread the fire.

Specific hazards arising from	Contents under pressure. Pressurized container may explode when exposed to heat or flame.

the chemical	During fire, gases hazardous to health may be formed.

Special protective equipment	Firefighters must use standard protective equipment including flame retardant coat, helmet with

and precautions for firefighters	face shield, gloves, rubber boots, and in enclosed spaces, SCBA.

Fire fighting	In case of fire: Stop leak if safe to do so. Do not move cargo or vehicle if cargo has been exposed

equipment/instructions	to heat. Move containers from fire area if you can do so without risk. Containers should be cooled

with water to prevent vapor pressure build up. For massive fire in cargo area, use unmanned hose

holder or monitor nozzles, if possible. If not, withdraw and let fire burn out.

Specific methods

General fire hazards

Use standard firefighting procedures and consider the hazards of other involved materials. Move containers from fire area if you can do so without risk. In the event of fire and/or explosion do not breathe fumes.

Extremely flammable aerosol. Contents under pressure. Pressurized container may explode when exposed to heat or flame.

Safety Data Sheet

6. ACCIDENTAL RELEASE MEASURES

Personal precautions, protective equipment and emergency procedures

Keep unnecessary personnel away. Keep people away from and upwind of spill/leak. Keep out of low areas. Many gases are heavier than air and will spread along ground and collect in low or confined areas (sewers, basements, tanks). Wear appropriate protective equipment and clothing during clean-up. Do not breathe mist or vapor. Emergency personnel need self-contained breathing equipment. Do not touch damaged containers or spilled material unless wearing appropriate protective clothing. Ventilate closed spaces before entering them. Local authorities should be advised if significant spillages cannot be contained. For personal protection, see section 8 of the SDS.

Methods and materials for containment and cleaning up

Environmental precautions

Refer to attached safety data sheets and/or instructions for use. Eliminate all ignition sources (no smoking, flares, sparks, or flames in immediate area). Keep combustibles (wood, paper, oil, etc.) away from spilled material. Stop leak if you can do so without risk. Move the cylinder to a safe and open area if the leak is irreparable. Isolate area until gas has dispersed. Cover with plastic sheet to prevent spreading. Absorb in vermiculite, dry sand or earth and place into containers. Prevent entry into waterways, sewer, basements or confined areas. Following product recovery, flush area with water.

Small Spills: Wipe up with absorbent material (e.g. cloth, fleece). Clean surface thoroughly to remove residual contamination. For waste disposal, see section 13 of the SDS.

Avoid release to the environment. Prevent further leakage or spillage if safe to do so. Avoid discharge into drains, water courses or onto the ground. Inform appropriate managerial or supervisory personnel of all environmental releases.

7. HANDLING AND STORAGE

Precautions for safe handling Obtain special instructions before use. Do not handle until all safety precautions have been read and understood. Pressurized container: Do not pierce or burn, even after use. Do not use if spray button is missing or defective. Do not spray on a naked flame or any other incandescent material. Do not smoke while using or until sprayed surface is thoroughly dry. Do not cut, weld, solder, drill, grind, or expose containers to heat, flame, sparks, or other sources of ignition. All equipment used when handling the product must be grounded. Do not re-use empty containers. Do not breathe mist or vapor. Avoid contact with eyes, skin, and clothing. Avoid prolonged exposure. When using, do not eat, drink or smoke. Pregnant or breastfeeding women must not handle this product. Should be handled in closed systems, if possible. Use only in well-ventilated areas. Wear appropriate personal protective equipment. Wash hands thoroughly after handling. Avoid release to the environment. Wash contaminated clothing before reuse. Observe good industrial hygiene practices.

Level 2 Aerosol.

Conditions for safe storage, including any incompatibilities

Store locked up. Pressurized container. Protect from sunlight and do not expose to temperatures exceeding 50°C/122 °F. Do not puncture, incinerate or crush. Do not handle or store near an open flame, heat or other sources of ignition. This material can accumulate static charge which may cause spark and become an ignition source. Secure cylinders in an upright position at all times, close all valves when not in use. Store in a well-ventilated place. Store away from incompatible materials (see Section 10 of the SDS).

Safety Data Sheet

8. EXPOSURE CONTROLS/PERSONAL

PROTECTION

|  | US. OSHA Table Z-1 Limits for Air Contaminants (29 CFR 1910.1000) | Value |
| --- | --- | --- |
|  | Components | Type |  |
|  | ETHYLBENZENE (CAS | PEL | 435 mg/m3 |
| 100-41-4) |  |  |
|  |  |  | 100 ppm |
|  | HEPTANE (CAS 142-82-5) | PEL | 2000 mg/m3 |
|  |  |  | 500 ppm |
|  | XYLENE (CAS 1330-20-7) | PEL | 435 mg/m3 |
|  |  |  | 100 ppm |
| US. ACGIH Threshold Limit Values Components |  |
|  |  | Type | Value |
|  | ETHYLBENZENE (CAS | TWA | 20 ppm |
| 100-41-4) |  |  |
|  | HEPTANE (CAS 142-82-5) | STEL | 500 ppm |
|  |  | TWA | 400 ppm |
|  | XYLENE (CAS 1330-20-7) | STEL | 150 ppm |
|  |  | TWA | 100 ppm |
|  | US. NIOSH: Pocket Guide to Chemical Hazards |  |
|  | Components | Type | Value |
|  | ETHYLBENZENE (CAS | STEL | 545 mg/m3 |
| 100-41-4) |  |  |
|  |  |  | 125 ppm |
|  |  | TWA | 435 mg/m3 |
|  |  |  | 100 ppm |
|  | HEPTANE (CAS 142-82-5) | Ceiling | 1800 mg/m3 |
|  |  |  | 440 ppm |
|  |  | TWA | 350 mg/m3 |
|  |  |  | 85 ppm |
|  | US. Workplace Environmental Exposure Level (WEEL) Guides |  |
|  | Components | Type | Value |
|  | DIMETHYL |  |  |
|  | ETHER (CAS | TWA | 1880 mg/m3 |
| 115-10-6) |  |  |
|  |  |  | 1000 ppm |
| Biological limit values |  |  |  |  |
|  | ACGIH Biological Exposure Indices |  |  |  |
|  | Components | Value | Determinant | Specimen | Sampling Time |
|  | ETHYLBENZENE (CAS | 0.15 g/g | Sum of | Creatinine in | * |
| 100-41-4) |  | mandelic acid | urine |  |
|  |  |  | and |  |  |
|  |  |  | phenylglyoxylic |  |  |
|  |  |  | acid |  |  |
|  | XYLENE (CAS 1330-20-7) | 1.5 g/g | Methylhippuric | Creatinine in | * |
|  |  |  | acids | urine |  |

* - For sampling details, please see the source document.

Safety Data Sheet

Appropriate engineering	Good general ventilation (typically 10 air changes per hour) should be used. Ventilation rates

controls	should be matched to conditions. If applicable, use process enclosures, local exhaust ventilation,

or other engineering controls to maintain airborne levels below recommended exposure limits. If

exposure limits have not been established, maintain airborne levels to an acceptable level. Eye

wash facilities and emergency shower must be available when handling this product.

Individual protection measures, such as personal protective	equipment

Eye/face protection	Wear safety glasses with side shields (or goggles).

Skin protection Hand protection

Other Respiratory protection Thermal hazards

General hygiene considerations

Wear appropriate chemical resistant gloves. Suitable gloves can be recommended by the glove supplier.

Wear appropriate chemical resistant clothing.

In case of insufficient ventilation, wear suitable respiratory equipment.

Wear appropriate thermal protective clothing, when necessary.

When using do not smoke. Always observe good personal hygiene measures, such as washing after handling the material and before eating, drinking, and/or smoking. Routinely wash work clothing and protective equipment to remove contaminants.

9. PHYSICAL AND CHEMICAL PROPERTIES

Appearance

Physical state

Form

Color

Odor

Odor threshold pH

Melting point/freezing point

Initial boiling point and boiling range

Flash point Evaporation rate

Flammability (solid, gas)

Liquid.

Aerosol. Liquefied gas.

Not available.

Not available. Not available. Not available.

-222.7 °F (-141.5 °C) estimated -12.68 °F (-24.82 °C) estimated

-42.0 °F (-41.1 °C) estimated Not available.

Not applicable.

Upper/lower flammability or explosive limits

Flammability limit - lower	3.4 % estimated

(%)

Flammability limit - upper	27 % estimated

(%)

Explosive limit - lower (%)	Not available.

Explosive limit - upper (%)	Not available.

Vapor pressure	3268.25 hPa estimated

Vapor density	Not available.

Relative density	Not available.

Solubility(ies)

Solubility (water)	Not available.

Partition coefficient	Not available.

(n-octanol/water)

Auto-ignition temperature	662 °F (350 °C) estimated

Decomposition temperature	Not available.

Viscosity	Not available.

Safety Data Sheet

Other information

Density	6.26 lbs/gal

Flammability class	Flammable IA estimated

Heat of combustion (NFPA	24.78 kJ/g estimated

30B)

Percent volatile	97.19

Specific gravity	0.75

VOC	5.5441269 lbs/gal Regulatory

600.291084 g/l Material

5.0096719 lbs/gal Material

664.332917 g/l Regulatory

10.  STABILITY AND REACTIVITY

Reactivity Chemical stability

Possibility of hazardous reactions

Conditions to avoid Incompatible materials

Hazardous decomposition products

The product is stable and non-reactive under normal conditions of use, storage and transport. Material is stable under normal conditions.

No dangerous reaction known under conditions of normal use.

Heat. Avoid temperatures exceeding the flash point. Contact with incompatible materials. Strong acids. Strong oxidizing agents. Halogens.

No hazardous decomposition products are known.

11.  TOXICOLOGICAL INFORMATION

| Information on likely routes of exposure |  |
| --- | --- |
| Inhalation | May cause damage to organs through prolonged or repeated exposure by inhalation. May cause |
|  | drowsiness and dizziness. Headache. Nausea, vomiting. Prolonged inhalation may be harmful. |
| Skin contact | Harmful in contact with skin. Causes skin irritation. |  |
| Eye contact | Causes eye irritation. |  |

Respiratory or skin sensitization

Respiratory sensitization

Skin sensitization

Safety Data Sheet

Ingestion

Symptoms related to the physical, chemical and toxicological characteristics

Expected to be a low ingestion hazard.

Headache. May cause drowsiness and dizziness. Nausea, vomiting. Irritation of eyes. Exposed individuals may experience eye tearing, redness, and discomfort. Skin irritation. May cause redness and pain.

| Information on toxicological effects |  |
| --- | --- |
| Acute toxicity | Harmful in contact with skin. Narcotic effects. |  |
| Components | Species |  |
| DIMETHYL ETHER (CAS 115-10-6) |  |  |
| Acute |  | Test Results |
| Inhalation |  |  |
| LC50 | Mouse | 494 ppm, 15 Minutes |
|  |  | 386 ppm, 30 Minutes |
|  | Rat | 308.5 mg/l, 4 Hours |
| ETHYLBENZENE (CAS 100-41-4) |  |  |
| Acute |  |  |
| Dermal |  |  |
| LD50 | Rabbit | 17800 mg/kg |
| Oral |  |  |
| LD50 | Rat | 3500 mg/kg |
| HEPTANE (CAS 142-82-5) |  |  |
| Acute |  |  |
| Inhalation |  |  |
| LC50 | Rat | 103 mg/l, 4 Hours |
| LD50 | Mouse | 75 mg/l, 2 Hours |
| XYLENE (CAS 1330-20-7) |  |  |
| Acute |  |  |
| Dermal |  |  |
| LD50 | Rabbit | > 43 g/kg |
| Inhalation |  |  |
| LC50 | Mouse | 3907 mg/l, 6 Hours |
|  | Rat | 6350 mg/l, 4 Hours |
| Oral |  |  |
| LD50 | Mouse | 1590 mg/kg |
|  | Rat | 3523 - 8600 mg/kg |
| * Estimates for product may be based on additional component data not shown. |  |
| Skin corrosion/irritation | Causes skin irritation. |  |
| Serious eye damage/eye irritation | Causes eye irritation. |  |

Not a respiratory sensitizer.

This product is not expected to cause skin sensitization.

Germ cell mutagenicity

No data available to indicate product or any components present at greater than 0.1% are mutagenic or genotoxic.

Safety Data Sheet

Carcinogenicity	Suspected of causing cancer.

IARC Monographs. Overall Evaluation of Carcinogenicity

ETHYLBENZENE (CAS 100-41-4)	2B Possibly carcinogenic to humans.

XYLENE (CAS 1330-20-7)	3 Not classifiable as to carcinogenicity to humans.

OSHA Specifically Regulated Substances (29 CFR 1910.1001-1050)

Not listed.

Reproductive toxicity	Components in this product have been shown to cause birth defects and reproductive disorders in

laboratory animals. Suspected of damaging fertility or the unborn child.

Specific target organ toxicity -	May cause drowsiness and dizziness.

single exposure

Specific target organ toxicity -	Causes damage to organs through prolonged or repeated exposure.

repeated exposure

Aspiration hazard	Not an aspiration hazard.

Chronic effects	Causes damage to organs through prolonged or repeated exposure. Prolonged inhalation may be

harmful. Prolonged exposure may cause chronic effects.

12.  ECOLOGICAL INFORMATION

| Ecotoxicity | Toxic to aquatic life with long lasting effects. |  |
| --- | --- | --- |
|  | Components |  | Species | Test Results |
|  | ETHYLBENZENE (CAS 100-41-4) |  |  |
|  | Aquatic |  |  |  |
|  | Crustacea | EC50 | Water flea (Daphnia magna) | 1.37 - 4.4 mg/l, 48 hours |
|  | Fish | LC50 | Fathead minnow (Pimephales promelas) | 7.5 - 11 mg/l, 96 hours |
|  | HEPTANE (CAS 142-82-5) |  |  |  |
|  | Aquatic |  |  |  |
|  | Fish | LC50 | Mozambique tilapia (Tilapia | 375 mg/l, 96 hours |
|  |  |  | mossambica) |  |
|  | XYLENE (CAS 1330-20-7) |  |  |  |
|  | Aquatic |  |  |  |
|  | Fish | LC50 | Bluegill (Lepomis macrochirus) | 7.711 - 9.591 mg/l, 96 hours |

* Estimates for product may be based on additional component data not shown. Persistence and degradability No data is available on the degradability of this product.

Bioaccumulative potential

Partition coefficient n-octanol / water (log Kow)

| DIMETHYL ETHER | 0.1 |
| --- | --- |
| ETHYLBENZENE | 3.15 |
| HEPTANE | 4.66 |
| XYLENE | 3.12 - 3.2 |
| Mobility in soil | No data available. |
| Other adverse effects | No other adverse environmental effects (e.g. ozone depletion, photochemical ozone creation |
|  | potential, endocrine disruption, global warming potential) are expected from this component. |

13.  DISPOSAL CONSIDERATIONS

| Disposal instructions | Collect and reclaim or dispose in sealed containers at licensed waste disposal site. Contents |  |
| --- | --- | --- |
|  | under pressure. Do not puncture, incinerate or crush. Do not allow this material to drain into |  |
|  | sewers/water supplies. Do not contaminate ponds, waterways or ditches with chemical or used |
|  | container. Dispose of contents/container in accordance with local/regional/national/international |
|  | regulations. |  |
| Local disposal regulations | Dispose in accordance with all applicable regulations. |  |

Safety Data Sheet

Hazardous waste code

Waste from residues / unused products

Contaminated packaging

The waste code should be assigned in discussion between the user, the producer and the waste disposal company.

Dispose of in accordance with local regulations. Empty containers or liners may retain some product residues. This material and its container must be disposed of in a safe manner (see: Disposal instructions).

Since emptied containers may retain product residue, follow label warnings even after container is emptied. Empty containers should be taken to an approved waste handling site for recycling or disposal. Do not re-use empty containers.

14.  TRANSPORT INFORMATION

DOT

UN number

UN proper shipping name

Transport hazard class(es) Class

Subsidiary risk Label(s)

Packing group

Special precautions for user

Special provisions

Packaging exceptions

Packaging non bulk

Packaging bulk

UN1950

Aerosols, Flammable

2.1

-

2.1

Not applicable.

Read safety instructions, SDS and emergency procedures before handling.

N82

306 None None

| IATA |  |
| --- | --- |
| UN number | UN1950 |
| UN proper shipping name | Aerosols, Flammable |
| Transport hazard class(es) |  |
| Class | 2.1 |
| Subsidiary risk | - |
| Label(s) | 2.1 |
| Packing group | Not applicable. |
| Environmental hazards | No. |

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

Other information

Passenger and cargo aircraft	Allowed

Cargo aircraft only	Allowed

Safety Data Sheet

IMDG

UN number	UN1950

UN proper shipping name	Aerosols, Flammable,

Transport hazard class(es)

Class	2.1

Subsidiary risk	-

Label(s)	2.1

Packing group	Not applicable.

Environmental hazards

Marine pollutant	Not applicable.

EmS	Not available.

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

Transport in bulk according to	Not established.

Annex II of MARPOL 73/78 and

the IBC Code

DOT

IATA; IMDG

General information	Avoid transport on vehicles where the load space is not separated from the driver's compartment. Ensure vehicle driver is aware of the potential hazards of the load and knows what to do in the event of an accident or an emergency. Before transporting product containers: Ensure that containers are firmly secured.  Ensure valve outlet cap nut or plug (where provided) is correctly fitted. Ensure adequate ventilation. Ensure compliance with applicable regulations

Safety Data Sheet

15.  REGULATORY INFORMATION

| US federal regulations | This product is a "Hazardous Chemical" as defined by the OSHA Hazard Communication |
| --- | --- |
|  |  | Standard, 29 CFR 1910.1200. |  |  |  |
| TSCA Section 12(b) Export Notification (40 CFR 707, Subpt. D) |  |  |
|  | Not regulated. |  |  |  |  |
| CERCLA Hazardous Substance List (40 CFR 302.4) |  |  |  |
|  | DIMETHYL ETHER (CAS 115-10-6) | Listed. |  |  |
|  | ETHYLBENZENE (CAS 100-41-4) | Listed. |  |  |
|  | HEPTANE (CAS 142-82-5) |  | Listed. |  |  |
|  | XYLENE (CAS 1330-20-7) |  | Listed. |  |  |
| SARA 304 Emergency release notification |  |  |  |
|  | Not regulated. |  |  |  |  |
| OSHA Specifically Regulated Substances (29 CFR 1910.1001-1050) |  |  |
|  | Not listed. |  |  |  |  |
| Superfund Amendments and Reauthorization Act of 1986 (SARA) |  |  |
| Hazard categories | Immediate Hazard - Yes |  |  |  |
|  |  | Delayed Hazard - Yes |  |  |  |
|  |  | Fire Hazard - Yes |  |  |  |
|  |  | Pressure Hazard - No |  |  |  |
|  |  | Reactivity Hazard - No |  |  |  |
|  | SARA 302 Extremely hazardous substance |  |  |  |
|  | Not listed. |  |  |  |  |
| SARA 311/312 Hazardous | No |  |  |  |
| chemical |  |  |  |  |
| SARA 313 (TRI reporting) |  |  |  |  |
|  | Chemical name |  | CAS number | % by wt. |
|  | ETHYLBENZENE |  | 100-41-4 | 1 to <5 |
|  | XYLENE |  | 1330-20-7 | 1 to <5 |
| Other federal regulations |  |  |  |  |

Clean Air Act (CAA) Section 112 Hazardous Air Pollutants (HAPs) List

ETHYLBENZENE (CAS 100-41-4) XYLENE (CAS 1330-20-7)

Clean Air Act (CAA) Section 112(r) Accidental Release Prevention (40 CFR 68.130)

DIMETHYL ETHER (CAS 115-10-6)

Safe Drinking Water Act (SDWA)	Not regulated.

US state regulations

US. California Controlled Substances. CA Department of Justice (California Health and Safety Code Section 11100)

Not listed.

US. California. Candidate Chemicals List. Safer Consumer Products Regulations (Cal. Code Regs, tit. 22, 69502.3, subd. (a))

ETHYLBENZENE (CAS 100-41-4) XYLENE (CAS 1330-20-7)

US. Massachusetts RTK - Substance List

DIMETHYL ETHER (CAS 115-10-6)

ETHYLBENZENE (CAS 100-41-4) HEPTANE (CAS 142-82-5) XYLENE (CAS 1330-20-7)

US. New Jersey Worker and Community Right-to-Know Act

DIMETHYL ETHER (CAS 115-10-6)

ETHYLBENZENE (CAS 100-41-4) HEPTANE (CAS 142-82-5) XYLENE (CAS 1330-20-7)

Safety Data Sheet

US. Pennsylvania Worker and Community Right-to-Know Law

DIMETHYL ETHER (CAS 115-10-6)

ETHYLBENZENE (CAS 100-41-4)

HEPTANE (CAS 142-82-5)

XYLENE (CAS 1330-20-7)

US. Rhode Island RTK

DIMETHYL ETHER (CAS 115-10-6)

ETHYLBENZENE (CAS 100-41-4)

XYLENE (CAS 1330-20-7)

US. California Proposition 65

WARNING: This product contains a chemical known to the State of California to cause cancer.

US - California Proposition 65 - CRT: Listed date/Carcinogenic substance

ETHYLBENZENE (CAS 100-41-4)	Listed: June 11, 2004

| International Inventories |  |  |
| --- | --- | --- |
| Country(s) or region | Inventory name | On inventory (yes/no)* |
| Australia | Australian Inventory of Chemical Substances (AICS) | No |
| Canada | Domestic Substances List (DSL) | Yes |
| Canada | Non-Domestic Substances List (NDSL) | No |
| China | Inventory of Existing Chemical Substances in China (IECSC) | No |
| Europe | European Inventory of Existing Commercial |  |
|  |  | No |
|  | Chemical Substances (EINECS) |  |
| Europe | European List of Notified Chemical Substances (ELINCS) | No |
| Japan | Inventory of Existing and New Chemical Substances (ENCS) | No |
| Korea | Existing Chemicals List (ECL) | No |
| New Zealand | New Zealand Inventory | No |
| Philippines | Philippine Inventory of Chemicals and Chemical | No |
|  | Substances (PICCS) |  |
| United States & Puerto Rico | Toxic Substances Control Act (TSCA) Inventory | No |

*A "Yes" indicates that all components of this product comply with the inventory requirements administered by the governing country(s)

A "No" indicates that one or more components of the product are not listed or exempt from listing on the inventory administered by the governing country(s).

16.  OTHER INFORMATION, INCLUDING DATE OF PREPARATION OR LAST

REVISION

| Issue date | 09-21-2015 |
| --- | --- |
| Revision date | 06-30-2016 |
| Version # | 04 |
| HMIS® ratings | Health: 2* |
|  | Flammability: 4 |
|  | Physical hazard: 0 |
| NFPA ratings | Health: 2 |
|  | Flammability: 4 |
|  | Instability: 0 |
| Disclaimer |  |
|  | This information is based on our current knowledge and is believed to be accurate and reliable as of the date completed. It is intended to describe the product for the purposes of health, safety and environmental requirements only. The information given is designed only as a guidance for safe handling, use, processing, storage, transportation, disposal, and release is not to be considered a warranty or quality specification. Therefore, it should not be construed as guaranteeing any specific property of the product. The user is responsible to ensure safe conditions for handling, storage, and disposal of the product and to assume liability for loss, injury or damage due to improper use. |

# Text boxes

HUSKY GREEN FIN PRIMER AEROSOL

Safety Data Sheet

Prepared according to Federal Register / Vol. 77, No. 58 /  March 26, 2012 / Rules and Regulations